## Slide 1: MASTERING (VIRTUAL) NETWORKS A Case Study of Virtualizing Internet Lab
Avin Chen
Borokhovich Michael
Goldfeld Arik
Notes: Good afternoon.
My name is Michael Borokhovich, I'm a Master degree student at the Ben Gurion University in Israel.
I'm going to present a paper that I wrote with Dr. Chen Avin and Dr. Arie Goldfel.
Our paper describes the case study of developing, deploying and exploiting a virtual computer networks laboratory.
Such a laboratory can be used for teaching Computer Networks and Network Programming courses.
The main contribution of our work is providing an example of using virtualization to create an excellent learning facility along with saving costs, space, and energy.

## Slide 2: Agenda
Introduction
Related Work
Virtualization
Virtual Lab Design
Students’ & Administrator’s
Conclusions & Future Work

## Slide 3: Introduction
The need for computer networks lab
  Computer engineering
  Electrical engineering
  Communication systems engineering
Notes: So, why do we need a computer networks laboratory.
We want to learn how do computers exchange the information in the internet, how the routers on the way know the routes to the destination.
We want to learn how to configure those routers and computers to allow them to communicate. In addition we want to measure information rates and many other important papameters.

## Slide 4: Working in Network Lab
Assignment document
  Build network
Configure devices
  IP Addresses
  Routing protocols
Send messages
Capture messages
Take measurements
Notes: Before each lab session – assignment document with instructions
Capture messages (investigate message fields)
Take measurements (time…)

## Slide 5: Related Work
5
Physical (real) lab
Simulation
Virtualization (MLN, VMware, Virtual PC)
Emulabs

## Slide 6
6
Pros:
  Real equipment
  “Hands on”
Cons:
  Cost
  Space
  Time
  Energy
Physical (real) laboratory

## Slide 7: Related Work
7
Physical (real) lab
Simulation
Virtualization (MLN, VMware, Virtual PC)
Emulabs

## Slide 8
8
Pros:
  Scalable
  Cost effective
Cons:
  Not a real equipment
  Not a “hands on”
  Simulation tools are complex
Simulation (NS2, OPNET…)

## Slide 9: Related Work
9
Physical (real) lab
Simulation
Virtualization (MLN, VMware, Virtual PC)
Emulabs

## Slide 10: Virtualization
One physical machine
Many independent operating systems
Operating system = Virtual machine
Virtualization Platforms:
  Virtual PC
  VMware
  Xen

## Slide 11: Virtualization Benefits
11
Increase utilization
Lower number of physical machines
Isolation
Simple management
Different operating systems on a single computer
Notes: 11
Increase utilization
Lower number of physical servers
  reduce hardware maintenance costs and the energy saving
Isolation
  prevent one application from impacting another. If we want to isolate some applications (or just test some unstable application), we can easily run them on different virtual machines
Virtual machine can be easily duplicated
  speed up server deployment
Different operating systems on a single physical machine
  Linux, Windows,...

## Slide 12: Virtual Lab Design
“Mastering Networks” book of Liebeher and El Zakri
Set of equipment:
  4 PCs
  4 Routers
  8 Switches
We call this set - NetLab

## Slide 13: Virtual Lab Design
Instead of real NetLabs – virtual NetLabs
Single physical server
Virtualization platform - Xen
15 Virtual NetLabs
Xen allows many VM
Xen is freeware

## Slide 14: Students’ Perspective
Almost the same as real

## Slide 15: Students’ Perspective
Laboratory
Campus
Home
Anytime, anywhere

## Slide 16: Students’ Perspective
Building Networks

## Slide 17: Students’ Perspective
Access
  Virtual device – unique display number
  Remote access - VNC

## Slide 18: Students’ Perspective
Virtual PC
  Linux OS
  Graphical Desktop
Virtual Router
  Linux OS
  Quagga
  CISCO like

## Slide 19: Administrator’s Perspective
Topologies Preparation
  Simple text file defines the topology
Remote troubleshooting
  Restore VNC displays
  Restart machines
  Replace damaged machines
Administrator
Student

## Slide 20: Extended Topologies
Physical Lab – Small Networks
Virtual Lab – Any Networks
BGP lab
Multicast lab

## Slide 21: System Features
Capacity – more than 200 virtual machines (15 NetLabs)
Flexibility – any network topology
Remote Access – anytime, anywhere
Simple Administration
Fast Failure Recovery - everyone can be a “root”
In class lab sessions
Open Source/Freeware Software

## Slide 22: Lab Implementation
Equipment
  One Physical Server
Staff
  Linux Specialist
    Install Linux, Xen, Virtual Machines
  Lab Administrator
    Basic Linux and Networks knowledge
  Lab Instructor
    Networking and Linux knowledge

## Slide 23: Conclusions & Future Work
Conclusions
  Excellent students’ feedbacks
  Almost full “hands on” lab
  Saving cost, space, time and energy
  Easy administration
Future work
  Further experiments developing
  Increase system capacity
  Graphical interface to create topologies

## Slide 24: Thank You!

## Slide 25: System Architecture
Single HW server
  Intel Xeon Quad Core CPU x 2
  16 GB RAM
  Hard Disks 250 GB x 4
Virtualization
  Virtualization Platform - Xen
  Hosting OS – Debian Linux 4.0
  Guest OSs (Virtual Machines) – Debian Linux 4.0
    64 MB RAM
    Quagga Routing Suite
    Packet Tracing Software: Tcpdump, Wireshark